## Slide 1: Spatial and Temporal Mapping of Cervical Lesions Using Cervical Cell Lift ; A Two-Year Longitudinal Observation
M. Miyazaki1, N. Egawa1, A. Shirz2, A. Nishimura3, T. Motohara3,
K. Nagasaka4, R. Crawford2, J. Doorbar1.
1Cambridge University - Cambridge (United Kingdom),
2Cambridge University Hospital - Cambridge (United Kingdom),
3Kumamoto University - Kumamoto (Japan),
4Teikyo University - Tokyo (Japan)
Notes: Hello, My name is Mai Miyazaki from Cambridge University. I will present our two-year longitudinal observation using Cervical Cell Lift.

## Slide 2: Principle of Cervical Cell Lift: From Lesion Biology to Spatial Mapping
MCM / E4 staining and spatial mapping
Apply nitrocellulose membrane to cervix for 15 sec
Fixation
Cervical Cell Lift (CCL) = Non-invasive spatial mapping of cervical lesions while preserving epithelial topology
Enables grading & localization of lesions without biopsy
Capable of detecting HSIL
Methods
MCM+ = Proliferating cells
E4+ = Productive HPV infection
Can CCL track lesion changes over time and reduce the need for repeated biopsies?
Aim
HSIL
Productive HPV+
Os
DAPI E4 MCM
DAPI MCM E4
CIN2-3(HSIL)
CIN1(LSIL)
DAPI MCM E4
MCM/E4 patterns
in tissue lesions
Notes: First, let me briefly explain Cervical Cell Lift, or CCL.
CCL is a non-invasive method for spatial mapping of cervical lesions while preserving epithelial topology. The key concept is that LSIL and HSIL show different MCM and E4 patterns in tissue lesions. MCM highlights proliferating cells and indicates an HSIL-like pattern when it extends upward. E4 highlights productive HPV infection in superficial differentiated cells. The procedure is simple: a nitrocellulose membrane is applied to the cervix for 15 seconds, then fixed and stained. After scanning, these signals are converted into a spatial biomarker map. Our aim was to assess whether CCL can track lesion changes over time without repeated biopsies.

## Slide 3
Columnar
X-1M 1st Consultation
Conization
PI: Age：40, Cytology: HSIL, HPV67+
Patient Information and CCL–Cone Tissue Spatial Mapping
CIN3
Final histology: CIN3,
negative margins
TZ
ECT
LSIL
Metaplasia
HSIL
Normal
MCM>1/3
Basal only
MCM>2/3
IF
(MCM, E4 , p16)
Spatial Mapping
11-6’: MCM+
Os
DAPI E4 MCM
X
Notes: This is a 40-year-old woman with HSIL cytology and HPV67 positivity. One month before conization, CCL showed MCM-positive areas from 11 to 6 o’clock. Conization confirmed CIN3 with negative margins. We then compared the preoperative CCL map with the conization tissue map. On the right, the spatial maps show anatomical regions, histological lesion distribution, and upward MCM expression in the cone tissue. The CCL map showed good spatial concordance with the conization tissue, suggesting that CCL can reflect regional lesion distribution on the cervix.

## Slide 4
X-1M 1st Consultation
X
X+15M(LSIL)
X+30M(LSIL)
Two-Year Longitudinal Observation
0’, 5-6’: E4+
CIN1
CIN1
4-6’, 8-9’: MCM+
3’: E4+
6’: E4+, MCM+
Os
DAPI E4 MCM
Os
DAPI E4 MCM
Conization
CIN3
11-6’: MCM+
Os
DAPI E4 MCM
Final histology: CIN3,
negative margins
Notes: We then followed the same patient over two years. Before treatment, CCL showed a broad MCM-positive area, consistent with CIN3. After conization, cytology initially became negative.
However, LSIL cytology was detected again 15 months after the operation.
At the same time point, repeat CCL showed focal MCM-positive areas and E4 positivity. At 30 months, the dominant signal shifted toward E4-positive areas, suggesting productive HPV infection rather than a broad HSIL-like proliferative pattern.

## Slide 5
Discussion ＆ Conclusion
Spatial Mapping
Concordance with Histology
Non-invasive Follow-up
CCL could visualize biomarker distribution on the cervix non-invasively
Two-year follow-up showed spatial and temporal changes of the lesion
CCL spatial mapping showed concordance with conization histology in this case
This suggests CCL can reflect regional lesion distribution
CCL may support non-invasive follow-up and help reduce repeated biopsies
Larger studies are needed to confirm clinical usefulness
Notes: In conclusion, CCL visualized cervical biomarker distribution non-invasively. In this case, it showed spatial concordance with conization histology and captured temporal changes over two years. Larger studies are needed to confirm its clinical usefulness. Thank you.